## Slide 1: Network Protocol Analyzers
Comparison of tools and use case

## Slide 2: Contents
How it works
Protocol Analyzers
Use Case
Conclusion
Protocol Analyzers and uses cases
Wireshark vs tcpdump
4
1
2
3

## Slide 3: Overview
Network protocols
Protocol Analyzers
Use Case
Wireshark
tcpdump
Data get captured and analyzed by sniffing them on Layer 1 – wire level
A process of encapsulation – decapsulation as OSI Models describes occurs
Problem breakdown approach
Bottom-up
Narrowing the scope
Lessons & Answers

## Slide 4
OSI de-encapsulation process

## Slide 5
Criteria | Wireshark | tcpdump
Open-Source | + | +
Easy to use | + | -
Easy to Learn | + | -
Packet Identification analysis & decode | + | -
Efficiency decoding | + | -
Fast setup on the host | + | +
Filters | + | -
Network Interfaces | + | -
Cross-Compatibility | + | -
Flexibility on using live | + | +
Troubleshooting | + | +
Data capture abilities | + | +
Industry Standard | + | +
Product & Community Support | + | +
Wireshark vs tcpdump

## Slide 6
Chart: 
| Wireshark | tcpdump
Compare Results | 14 | 7
Open-Source
Open-Source
Easy to Learn
Easy to use
Data capture abilities
Fast setup on the host
Capture then use on Wireshark
CLI
It is not about the percentage. It is all about use case and infrastructure
Wireshark vs tcpdump

## Slide 7: Use cases
Network traffic analysis for statistics
Sniffing
troubleshooting
monitoring
Data analysis capture for decryption
And many much more

## Slide 8: Use cases
Wireshark main use case follows simple
rules of problem solving

## Slide 9: Use cases scenario 1
Unreal Engine Packaged Game Development mode client-server Session failure
2 Game Instances on separate machines – client & server fail to communicate with each other on same subnet. Server Successfully creates an online game session but client fails to connect to that listen game instance to be more precise it cannot find any local LAN session at all. (We conclude/assume that the client/server session setup from game-programming perspective is done correctly and there is not misconfiguration in that part but the problem is Network derived)

## Slide 10: Use cases scenario 1
Problem Thinking
When we face such problems first, we look into documentation of the framework/game engine to see which IP range the LAN packets are being sent (in which IP the server Listens and the clients should broadcast/multicast).
Let’s assume that we do not have such information for a reason, how we approach this kind of a problem?
Check the 2 Game instances on 1 local machine with a loopback adapter to see if they can successfully communicate join each other and from which IP as outbound/sent interface the multicast (mcast) or broadcast traffic is being generated/pushed-forward (using Network Traffic Analyzers).
Create an isolated Network Environment where broadcast or multicasts packets are being controlled and they are known for each of the service (if you use a regular/normal network environment then the packets will be too many and it will take a while until you recognize the proper ones that being generated from client for a find/join session plus you may introduce network congestion or Computer/program crash if the traffic is extremely high … always try to reproduce the problem under controlled environment)
Use a Network Analyzer to see the Network Traffic that being generated across the Network

## Slide 11: Use cases scenario 1
The Solution
Using Wireshark first we performed find/join operations from client game instance on a loopback to first catch the IP address that is being generated … it seems to be a simple broadcast with the pc/host domain name 255.255.255.255
We tried in another network adapters/interface as well such as wi-fi but for a strange reason there were not broadcast packets at all there.
But we detected that in VMware Network Adapter VMNetx (1, 2, 3... etc. depending on configuration) the broadcast packets appeared normally but not in wi-fi
This is more likely to be a Network priority interface problem to validate our thinking we opened a PowerShell session in windows 10 and typed the command: Get-NetIPInterface

## Slide 12: Use cases scenario 1
we can see that in the loopback adapter the interface that the traffic generated outbound was not in wi-fi at all but on vmnet adapter with that in mind we could disable it and try again until we see that wi-fi gets the traffic (priority issue)).

## Slide 13: Use cases scenario 1
So, this is the reason that broadcast packets did not select wi-fi adapter perhaps in order to solve this we either disable these interfaces (if it’s safe network operation wise) or change the metric on each one via GUI or CLI command

## Slide 14: Use cases scenario 1
GUI approach to change interface metrics

## Slide 15: Use cases scenario 2
A network where DHCP process had DO without RA

## Slide 16: Use cases scenario
Clients’s PC unable to get DHCP offer

## Slide 17: Use cases scenario
Server Logs shows that communication is ok
Up to a point

## Slide 18: Use cases scenario
Sniffing traffic by following the flow of the packet

## Slide 19: Use cases scenario
Sniffing traffic by following the flow of the packet

## Slide 20: Use cases scenario
Sniffing traffic by following the flow of the packet
In each segment
port forwarding the traffic and capture with Wireshark on top of WAN backhaul

## Slide 21: Use cases scenario
Sniffing traffic by following the flow of the packet
In each segment

## Slide 22: Use cases scenario
Main Firewall debug troubleshooting

## Slide 23: Use cases scenario
Firewall can reach DHCP server thought

## Slide 24: Use cases scenario
Misconfiguration of IP despite that was legit
(It could be reached)

## Slide 25: Use cases scenario
DORA SUCCESS

## Slide 26: Use cases scenario
DORA SUCCESS

## Slide 27: Conclusion
To understand a problem first we understand the application tier error then the network.
Doesn’t matter how big the network is, cut it up into chunks until you close in on the issue, it is like a shortest-route path algorithm logic, actually, this is exactly how an algorithm will work its way through the solution e.g., make neighbours, many times the same way we use to solves agnostic problems.
Trace the problem with appropriate methodology applied e.g., bottom top in OSI/TCP-IP layer [13].
Log the first point of failure
Log the Last Point of failure
Repeat
Wireshark is your friend
Common Logic behavior for problem solving.
To solve a problem
To Use a tool
Its about current infrastructure and design possibilities

## Slide 28: Thank You!